## Slide 1: VoIP UserAgent
SIP UserAgent written in Java
Maven Project - JavaFX Application
https://github.com/danielepelleg/VoIP

## Slide 2: What is it about?
User Agent VoIP
A User Agent is the fundamental element of the SIP protocol and allows the user to make calls using the IP protocol without a data transport connection.
SIP - Session Initiation Protocol
It is a text-based application-level protocol used to create, modify, or terminate sessions (such as VoIP sessions) between multiple participants. By default, it uses the UDP protocol.

## Slide 3: SIP Session
SIP Requests
INVITE
  used to initiate a VoIP session with the other party (the callee)
  may include media description via SDP
ACK
  confirms receipt of a final response to a previous INVITE request
BYE
  terminates a connection

## Slide 4: RTP Session
Real-time Transmission Protocol
End-to-end transport protocol for real-time applications, typically used over UDP. It does not establish sessions and can be used to transport any type of media or codec.
Header

## Slide 5: RTP Session
Real-time Transmission Protocol
End-to-end transport protocol for real-time applications, typically used over UDP. It does not establish sessions and can be used to transport any media or codec.
Audio Format
Sample Rate: 8000 Hz
Sample Size: 8 bit
Channel: 1
Packet Size: 8000 * 20 / 1000 = 160 bytes
Packet time: 20ms
Encoding: ULAW

## Slide 6: Diagrams
A high-level overview of the completed project

## Slide 7: Application - Use Case Diagram

## Slide 8: SIP - Class Diagram

## Slide 9: RTP - Class Diagram

## Slide 10: User Interface

## Slide 11: GUI
Displays the session logs. The Update button allows you to refresh the content of the textbox, while the Save button lets you save the content to src/main/resources/requests
Main window through which it’s possible to start the call.
The black label provides information on the call’s status.

## Slide 12: GUI
Settings page. Through this page, the user can view the session's IDs and tags, and change certain parameters such as their name and some sinusoidal wave settings.
Window for sending RTP packets. The first three buttons represent different audio transmission modes, while the button below allows you to stop the transmission.

## Slide 13: Let's get technical
The structure of the classes

## Slide 14
INVITE REQUEST
+
SDP
src/main/java/VoIP/Request.java

## Slide 15
src/main/java/VoIP/UserAgent.java

## Slide 16
RECEIVE RESPONSE
src/main/java/VoIP/Response.java

## Slide 17
src/main/java/VoIP/Response.java
RECEIVE RESPONSE

## Slide 18: Socket Timeout Exception
src/main/java/VoIP/UserAgent.java

## Slide 19: RTP Packet Class
src/main/java/Audio/RTPPacket.java

## Slide 20: AudioThread Class - Send Spoiled Audio
src/main/java/Audio/AudioThread.java

## Slide 21: AudioSinusoidalThread Class - Send Sinusoidal Audio
src/main/java/Audio/AudioSinusoidalThread.java

## Slide 22: AudioFileThread Class - Send File Audio
src/main/java/Audio/AudioFileThread.java